Qt on Devices
Girish Ramakrishnan (girish@forwardbias.in)

---
About me

---
The problem
- Getting Qt running on a device is a hassle
  - Edit mkspec
  - Apply gfx patches
  - Optimal Qt configuration
  - Deployment
- Kills the joy of developing with Qt

---
Vision
Qt needs to work out of the box for embedded boards without having to patch Qt and mkspecs

---
Technical goal
configure -device <device>

---
Step 1 – Compilation
- Why are mkspecs modified?
  - Sysroot
  - Compiler options
  - Path to xcompiler

---
Step 1 - solution
- Make -sysroot a supported option
  - Required changes to qmake and configure
  - Qt installs into sysroot
- Compiler options now part of mkspec
  - FP ABI, Multi arch etc
- Added -device-option
  - Specify xcompiler using -device-option CROSS_COMPILE=<compiler path>
- mkspec has a sanity check to check the setup
- Internals: load(device_config)

---
Step 1 - Compilation
- Pkg-config
  - Second class citizen in Qt4
  - -force-pkg-config only checks environment variables
  - When xcompiling, it's mandatory!

---
Step 1 - Solution
- Rewrote pkg-config support
  - -(force/no)pkg-config
- Environment variables automatically setup if absent by inspecting sysroot
  - Also saved as part of qdevice.pri

---
Step 2 – QPA Plugin
Make selection of the plugin automatic based on the device

---
Step 2 - Solution
Allow mkspecs to provide a default plugin

---
Step 3 - Display
- EGLFS is example code
  - EGLFS is platform dependent
- Configure has no idea of EGLFS or DirectFB

---
Step 3 - Solution
- Added config.test for configure
- Rewrote EGLFS to be able to create multiple windows, multiple contexts etc
  - Context menus work now
  - Support for transparency (qmlscene --transparent)
- EGLFS Hooks
  - Designed to not pollute the main eglfs plugin itself
  - Can specify depth, format, gl caps
  - GL Composed and Hardware cursor support
- DirectFB has similar design

---
Step 4 - Input
- Poor decision of GUI/Input handling split
  - -plugin EvdevKeyboard -plugin EvdevMouse:/dev/event/input0

---
Step 4 - Solution
- Evdev now part of eglfs
- EGLFS also works when no udev is present

---
Miscellaneous changes
- config.summary
- Wrote linuxfb qpa plugin

---
What's coming
- Allow -device spec to pass configure options
- Device optimizations
  - Hardware image decoding
  - Video to layer
  - Wayland/Generic cross buffer sharing
- Create host and target tools
- Support on-target compilation
- Serial port configuration

---
Summary
configure –device pi -sysroot <path> -device-option CROSS_COMPILE=<compiler>